# Text boxes

MS Viking Surf

MS Viking Surf – 70,40m Platform Supply Vessel. Delivered in December 2002 by West Contractors AS, Norway as yard no. 19 to Eidsurf AS, Bømlo, Norway. The design is by Vik & Sandvik AS, Fitjar, Norway. This vessel is the first VS470 of this new successful type made.

Principal particulars

Length o.a.:		70,40 m

Length p.p:		64,00 m

Breadth mid:		16,60 m

Depth to 1st. Deck:	7,60 m

Gross tonnage:		2409 GRT

Speed:		14,5 knots

Class:		DNV +1A1, SF, E0

### Propulsion system

Main Engines:	2 x MAK 8M25 (3264 hp)

Gear:	Rolls Royce 600 AGSC-KP /500HD

Propeller system:	Ulstein 30 P1/4T – 86 P1/4T

Shaft generators:	Leroy Somer LSA53 VS7, 1440kW

### Auxiliary engines

Main generators:	2 x Caterpillar 3406TA  345kW

Emergency diesel generator:	Caterpillar 3304NA 73kW

### Sidethrusters

Make:	Brunvoll

Fwd:	2 x AR-63-LNC-1650 (800 hp)

Aft:	2 x FU-63-LTC-1550 (800 hp)

#### Electronical equipment

Radar 1:	Furuno FAR-2825X     3CM

Radar 2:	Furuno FAR-2835S   10CM

Sat Nav./ Direction finder:	2 x Furuno GP80

Chart plotter 1:	Simrad ECDIS SPS-2000

Autopilot:	Robertson AP9 MK III

Gyrocompass:	2 x S.G.Brown Gyro

Log:	Furuno DS-80

Dynamic Positioning System:	Simrad SDP11

Radar Transponder	Sailor, Tron SART

Echo Sounder:	Furuno FE 700

GMDSS station:	Furuno RC66SA3

Weatherfax:	Navtex NX-500

Cellphones/fax	Nokia PremiCall GSM

Sat Phone/fax	Nera Inmarsat B

Onboard Phone System:	Siemens 3010

VHF:	Furuno/Sailor/Comrod

MF/HF/SSB Radio telephone	Furuno FS-5000

### Ship systems

F.O. and L.O. separators:	Alfa Laval

Air Compressors:	Atlas Copco LE-75 E250

Oily water separator:	Helisep M-2500

Vent./AC-arrangement:	Miljø-Teknikk AS

Fresh Water Generator:	Norwegian MT 10 T-35 T SRH

Fans:	Miljø-teknikk MPV 300 A1K

Engine room CO2 plant:	Alf Lea & Co

Main alarm system:	Aker Maritime IAS

Mob boat:	Mako 655 Jet, 225 hp Steyr

Liferafts:	6 x Viking 160DK+

Bulk storage system	Randaberg Sveiseservice

Ballastmonitoring system:	Aker Kværner IAS

Searchlights:	Norselight

Fire alarm:	Elteco

Rudders:	Rolls-Royce High Lift Flap Rudder

Steering Gears:	Rolls-Royce Tenfjord SR642

Switchboard:	450V - ABB

### Capacities

Fuel oil:	1070 m3

Fresh water:	858 m3

Water Ballast:	710 m3

Dry bulk:	340 m3

Accommodation:	32 men

Deck area:	680 m2

Deck load:	1600 tonnes

### Deck equipment

Deck Crane:	Hydramarine HMC1077  3T/12M

Tugger winch:	2 x Brattvaag LAKMS 41010  10T

Anchor windlass:	Brattvaag BFMG63044

MS Viking Surf