# Text boxes

MS Viking Athene

MS Viking Athene – 73,40m Platform Supply Vessel. Delivered in October 2006 by West Contractors AS, Ølensvåg, Norway as Yard no. 27 to Eidesvik AS, Bømlo, Norway. The design is by Vik & Sandvik AS, Fitjar, Norway.

Principal particulars

Length o.a.:		73,40 m

Length p.p:		64,00 m

Breadth mid:		16,60 m

Depth to 1st. Deck:	7,60 m

Gross tonnage		3550 GRT

Speed:		14,5 knots

Class:		DNV +1A1, SF, E0

### Propulsion system

Main Engines:	2 x MAK 8M25 (3264 hp)

Gear:	Scana Volda

Propeller system:	Scana Volda ACG68/600K

Shaft generators:	Pon Power

### Auxiliary engines

Main generators:	2 x Caterpillar 3406TA  345kW

Emergency diesel generator:	Caterpillar 3054T 73kW

### Sidethrusters

Make:	Brunvoll

Type:	4 x FU-63-LTC-1550 (1000 hp)

#### Electronical equipment

Radar 1:	Furuno FAR-2817

Radar 2:	Furuno FAR-2837S

Sat Nav./ Direction finder:	2 x Furuno GP90

Chart plotter 1:	Telko AS TECDIS

Autopilot:	Simrad AP-9

Gyrocompass:	3 x RGC80 Simrad

Speed Log:	Furuno DS-80

Dynamic Positioning System:	Kongsberg

Radar Transponder	Jotron, Tron SART

Echo Sounder:	Furuno FE 700

GMDSS station:	Furuno GMDSS A1, A2, A3

Weatherfax:	Furuno NX 700

Cellphones/fax	Ericsson F251

Sat Phone/fax	Telenor V-Sat + Nera Mini-M

Onboard Phone System:	Zenitel

VHF:	2 x Sailor RT2048

MF/HF/SSB Radio telephone	Furuno FS-1562-25

AIS	Furuno 150

UHF	Motorola GM360/GP340

### Ship systems

F.O. and L.O. separators:	Alfa Laval

Bulk Handl. Compressors:	Atlas Copc GA160W-100x

Oily water separator:	Jowa  3Sep OWS

Vent./AC-arrangement:	Aeron AS

Fresh Water Generator:	Enwa MT 10 T-35 T SRH

Fans:	MPV 300 A1K

Engine room CO2 plant:	Alf Lea & Co

Main alarm system:	Aker Kværner

Mob boat:	Norsafe 655 Mako

Liferafts:	6 x Viking 16DK+

Bulk storage system	Randaberg Sveiseindustrier AS

Ballastmonitoring system:	Wärtsilä Automation Norge AS

Searchlights:	AstraLux - Vassnes Elektro

Fire alarm:	Eltek

Rudders:	Rolls-Royce High Lift Flap Rudder

Steering Gears:	Rolls-Royce Tenfjord SR622

Switchboard:	450V - Wärtsilä

### Capacities

Fuel oil:	1050 m3

Fresh water:	780 m3

Methanol:	191m3

Water Ballast:	716 m3

Dry bulk:	340 m3

Accommodation:	32 men

Deck area:	680 m2

Deck load:	1600 tonnes

### Deck equipment

Deck Crane:	Hydramarine HMC1077 LT10-19 	(30-13)

Tugger winch:	2 x Brattvaag 41010 10T

Anchor windlass:	Brattvaag

MS Viking Athene